## Slide 1: Automatic Lens Smear Detection
Assignment 1
Submitted By:
Arpit Hasmukhbhai Patel – A20424085
Hitanshu Rami – A20458137
Hariharan Shankar - A20442562

## Slide 2: Introduction
Detection of Smear on a Camera lens is one of the most important necessity of the mapping companies.
Cleaning the camera lens or choosing to retake the photos is not efficient and costly especially when it is being used for security or underwater.
Hence, it is requisite that we detect a blur that is caused by smear on the lens.

## Slide 3: Aim
For this assignment, the idea is to create a mask which shows the smear on each camera.
The cameras film a sequence of street views from different angles.
With input being a sequence of street view images, the output is a mask of the smear on the lens.

## Slide 4: Approach
Step 1 : First, We read all the images from the given folder and average it, so we get an average image of all the input images.
What is Image Averaging?
To enrich video images that are degraded by random noise, a digital image processing technique called Image Averaging is widely used.
It operates by calculating the arithmetic mean of the intensity values for each pixel position in a cluster of captured images from the same view field.
Why do we use Image Averaging?
Each corrupted image has a stable signal component and a random noise component. In the averaging process, the signal component of the image remains the same, but the noise component differs from one image frame to another. Because the noise is random, it tends to cancel during the summation.

## Slide 5: Approach
Step 2: We convert the image into grayscale and then apply Gaussian Filter Smoothing.
What is Gaussian Smoothing?
Gaussian smoothing is a 2D convolution operator that is used to `blur` the images and reduce detail and noise.
We then pass this image frame for binarization.

## Slide 6: Approach
Step 3 : Converting the image into a binary image using Adaptive Thresholding.
How does Adaptive Thresholding work?
Adaptive thresholding is the method where the threshold value is calculated for smaller regions and therefore, there will be different threshold values for different regions.
It calculates the local threshold value of a region of an image using the pixel values of its neighbors.
Instead of calculating a single global threshold for the entire image, several thresholds are calculated for every pixel by using a specific formulae that take into account the mean and standard deviation of the local neighborhood

## Slide 7: Approach
Step 4: Lastly we erode and dialte the final results so noise found in the average image found, before we project the final mask. Because sometimes the might detect noise as a smear so we erode and dilate to check for depth of it. If it is just noise it will erode else that will appear in final mask. Hence Smear is Detected.

## Slide 8: Results
Average Mean Image
Smoothened Mean Image
Final Mask

## Slide 9: Results
Average Mean Image
Smoothened Mean Image
Final Mask

## Slide 10: Results
Average Mean Image
Smoothened Mean Image
Final Mask

## Slide 11: Results
Average Mean Image
Smoothened Mean Image
Final Mask

## Slide 12: Results
Average Mean Image
Smoothened Mean Image
Final Mask

## Slide 13: Conclusion
As a result of averaging all the images, the edges that are not present in every image in the cluster of images will turn white. That means that edges that are constant from image to image will remain black.
The region(spotted) white on final image is due to smear on camera lens was then detected.

## Slide 14: References
Kenneth R. Spring, John C. Russ,Matthew Parry-Hill, Thomas J. Fellers, and Michael W. Davidson, Image Averaging and Noise Removal Article on Olympus.
http://docs.opencv.org/trunk/da/d22/tutorial_py_canny.html
http://miriamposner.com/classes/medimages/3-use-opencv-to-find-the-average-color-of-an-image/
A. Jaiswal, B. Garg, V. Kaushal and G. K. Sharma, "SPAA-Aware 2D Gaussian Smoothing Filter Design Using Efficient Approximation Techniques," 2015 28th International Conference on VLSI Design, Bangalore, 2015, pp. 333-338.
J. Canny, "A Computational Approach to Edge Detection," in IEEE Transactions on Pattern Analysis and Machine Intelligence, vol. PAMI-8, no. 6, pp. 679-698, Nov. 1986.